## Slide 1: NSWI170: Lab 03 Buttons Controlling LEDs
Martin Kruliš
Notes: https://media.makeameme.org/created/buttons-buttons-everywhere.jpg

## Slide 2: Revision
LEDs
  Pins must be set to output pinMode(led1_pin, OUTPUT);
  Digital write changes state digitalWrite(led1_pin, HIGH);
    HIGH ~ off, LOW ~ on (better use ON/OFF constants)
  Use constants instead of numeric literals!
    led1_pin instead of 13
  Do not repeat yourselves!
    Make good use of functions, loops, arrays…

## Slide 3: Bit Encoder
Task 1: Bit-wise LED Encoder
  Write a function that takes integer and changes the LED states according to its lower 4 bits
    0 ~ LED is off, 1 ~ LED is on
  Useful to remember
    Bitwise operators: & (AND), | (OR), ~ (negation)
    Bit shifts <<, >>
  Test it (try to display some constant values)
5 = 0101b =
11 = 1011b =
21 = 10101b =
Notes: Bit operations are also available as Arduino functions (bit(), bitRead(), bitSet(), bitClear()). You may use these functions instead of C-operators, but make sure you know, how to implement them (since you might need them for other things than Arduino).

## Slide 4: Continuous Counting
Task 2: Continuous Counting
  Create counter that continuously increments its self (modulo 16)
    With reasonable interval (e.g., 1s)
    Use the same approach as in Lab02 (avoid delay())
  Display the value of the counter on LEDs
    Using the function from Task 1

## Slide 5: Buttons
Setup
  pinMode(button1_pin, INPUT)
    Actually, this should be the default, but do it anyway
Get button state
  digitalRead(button1_pin)
    Inverse logic (false ~ button is pressed)
  Need to be checked periodically in the main loop
    Note that buttons are not perfect. It might happen that when a button is pressed/released, it creates a short oscillation effect (as if the button is pressed and released in quick succession a few times).
Notes: Hint: when you read the state of the button, save its state into variable if you need to use it multiple times. Repetitive calls to digitalRead() within one iteration of main loop are slow and you might get different results (as the actual state of the button may change in the middle of the loop).

## Slide 6: Buttons Controlling Counter
Task 3: Increment when button is pressed
  Update the code so the counter is incremented only when the button #1 is being pressed (is held down)
  The speed of the update should remain the same
Small improvement
  The counter is incremented the moment the button is pressed and then it continues in regular intervals

## Slide 7: Buttons Controlling Counter
Task 4:
  Stop automatically (continuously) incrementing the counter
  Counter should increment only when the button #1 is pressed (once)
    I.e., when the button state changes from not pressed to pressed
    Keep the copy of last known state of the button in global variable to find out when the state is changing

## Slide 8: Buttons Controlling Counter
Task 5: Decrement
  Make the second button work in a similar manner like the first one, only it will decrement the counter
  Note: How do you decrement in modulo arithmetic?
    x = (x + 15) % 16
Side task
  Make the third button add 5 to the counter
  Do you see the pattern (all three buttons are doing almost the same)?
    If your code seems redundant, simplify it!
It is almost like increment
Notes: Side task hint: use arrays for all button-related variables and constants (button pin, button last state, increment value).

## Slide 9: Smart Buttons
Task 6: Making buttons smarter
  Buttons will still increment/decrement the counter when pressed
  If the button is held for a while it starts to increment/decrement the counter continuously
    There should be 2 delay constants – how long before the continuous update start and how fast it proceeds (e.g., it starts after 1s and increments every 300ms)
    Do not use delay()!
  Remember there is more than 1 button
    You need to time operations of each button independently
This is today’s final assignment, details are in ReCodEx

## Slide 10: Structures
Better code encapsulation
  struct Button {
  int pin;
  bool down;
  unsigned long whenPressed;
  };
  struct Button buttons[3];
  void doSomethingWithButton(Button &button) {
  if (button.isDown) ...
  }
Structure encapsulates data
Passing by reference
(global variables may be accessed only from loop() and setup())
Dot notation to access properties

## Slide 11: Classes
For advanced C++ programmers
  class Button {
  private:
  bool down;
  public:
  bool isDown() {
  return down;
  }
  };
Almost the same as struct (in C++ we prefer classes)
Visibility specifiers (can be used in struct too, but in struct, public is the default)
Method – a function associated with class (can see member variables)

## Slide 12: Bonuses
Bonus 1: Alternating behavior
  Make the third button switch between the three implemented strategies of updating the counter
    Represented by tasks 3, 4, and 6
Bonus 2: Larger counter
  Allow the counter to grow from 0 to 256
  LEDs will alternate to show the lower 4 bits and higher 4 bits of the counter in an interval (if no button is pressed)
    E.g., alternating every 1 second or when button 3 is pressed

## Slide 13: Bonuses
Bonus 3: Debouncing
  Deal with the button oscillation problem
  Set up a short debouncing interval
    Starts when button state changes
    Following changes are ignored until the end of interval
    Set up the constant wisely (1-20 ms sounds right)
      Smaller values may not be enough
      Larger values make the controls somewhat sluggish
Make the buttons implementation re-usable
  Might prove handy for subsequent assignments

## Slide 14: Discussion