## Slide 1: NSWI170: Lab 04 Displaying 7-seg Digits
Martin Kruliš

## Slide 2: Display
Warmup – prepare bitmasks for all digits
  Remember 1 ~ LED off, 0 ~ LED on (0b10000000 = digit 8)
DP
G
F
E
D
C
B
A
Segments encoded in byte
Verify your bitmasks (see constant digits in funshield library)
Everything but DP is ON

## Slide 3: Shift Register
74HC959D Shift Registers
  Serial input (sequence of bits), parallel output
  Input is controlled by a clock signal
  See https://en.wikipedia.org/wiki/Shift_register

## Slide 4: Fun Shield Display
Shift Registers Controlling Display
7 segment mask
Bits 0-3 indicate which digits are
active
Arduino feed
(data + clock)
Two connected 8-bit shift registers
Only one mask can be displayed at a time
Given mask may be displayed at selected positions

## Slide 5: Using Shift Registers
Controlling the output latch
  Outputs are cached (pins do not change)
  Raising edge triggers the update
    We need to do this to make any change “visible”
  digitalWrite(latch_pin, LOW)
  digitalWrite(latch_pin, HIGH)
Sending the data
  shiftOut(data_pin, clock_pin, bitOrder, value)
    bitOrder = MSBFIRST or LSBFIRST
    value = byte (8 bits) to be send bit-by-bit
Do not forget setting the pins to output

## Slide 6: Using Shift Registers
Algorithm
  Send the segment mask value (1 byte)
    Use MSBFIRST order
  Send which positions are active (1 byte)
    In MSBFIRST, positions correspond to lower bits
  Trigger the latch
    Set it to LOW then to HIGH
    Data loaded by previous steps will be sent to outputs (i.e., the digit will appear on the display)

## Slide 7: Display Counter Value
Preparation
  Write a function displayDigit(byte digit, byte pos)
  Implement the algorithm from the previous slide
Task 1
  Use your code from labs #03 (any version of buttons incrementing the counter)
  Modify it so that
    Counter goes only from 0-9
    Display the counter value as the rightmost digit of the 7-seg display (remaining digits must be blank) using the displayDigit()

## Slide 8: Changing Digit Position
Task 2
  Modify the counter to run modulo 10000
    Formatted as 4-digit number with leading zeros
    Make sure you handle the modular arithmetic correctly
  One digit (position) is shown at a time
    Rightmost digit (units) at start
    Button 3 changes the digit/order in loop (1, 10, …)
  Buttons 1 and 2 increment/decrement selected digit
    I.e., button 1 performs +1, +10, +100, or +1000, based on which order is selected (displayed)
      Button 2 analogically (-1, -10, …)
This is today’s final assignment, details are in ReCodEx

## Slide 9: Bonuses
Waiting Animation
  Create a “snake” animation that goes round the whole display
    Only one LED is on at any given time
    The snake should move using constant velocity and complete the cycle in exactly 1s
Prepare 7seg masks for letters
  Some letters need to be lowercased, some uppercased, be creative
  Use it to spell out “hello world” message letter by letter using single display position

## Slide 10: Discussion