## Slide 1: NSWI170: Lab 05 Display Multiplexing
Martin Kruliš

## Slide 2: Initial State
Take your code from Labs #4
  Counter works from 0-9999
    Only one digit is displayed at a time
  Button 1/2 increments/decrements the counter
    At displayed position
  Button 3 changes the visible digit

## Slide 3: Displaying all 4 digits
Task 1: Naïve approach
  Remove the functionality of button 3
    And button 1 and 2 will always do only +1/-1
  Display all 4 digits in every loop
    One by one in a sequence
Observation:
  Do you see any anomaly in the behavior of the LEDs?
  If not, try to put delay(2) at the end of loop()
  Yes, one of the digits (the one being displayed last) is actually brighter (since it lingers longer)

## Slide 4: Displaying all 4 digits
Task 2: Equalizing brightness
  Display one digit at a time in each loop
    Loop over the digits evenly
    Make sure each loop takes the same amount of time (do not forget to remove the delay())
  Make an interface for the display (separated from the rest of your code)
    Structure that holds display state with two functions:
      One that sets the internal number
      Second which is called repeatedly in every loop() to display the current number
        Automatically alternates visible digit on every call
On average!
Notes: It is completely sufficient to change the displayed digit (position 0-3) in every loop without additional timing. Assuming the only other actions handled in loop are button processing and subsequent state changes (i.e., some loops may be slightly slower than others, but they take approximately the same amount of time on average).
Btw. do not try some “smart” optimizations. For instance, when showing number 1000, one might think that we can display ‘000’ together. However, doing so would require much more sophisticated code if we want to ensure that all digits glow about the same and it is very difficult to get it right (especially for the ReCodEx assignment).

## Slide 5: Displaying all 4 digits
Task 3: Improving Appearance
  Do not display leading zeroes
    12 is displayed as 12 (aligned to the right), not as 0012
    Do not forget that 0 is still displayed as 1 digit
  Update the display structure to include decimal dot
    To be displayed at given position
    A method that sets its location
      Rightmost dot should probably not be displayed
  Test the new interface
    Button 3 can shift the position of the dot, for example

## Slide 6: Stopwatch
Task 4: Create Stopwatch
  The visible precision is 100ms (i.e., 0.1s)
    Internal precision should be at least 1ms (use millis() for correct timing)
    Use decimal dot to separate the last digit
    Always display at least 2 digits (zero is 0.0)
  Button 1 starts/stops the stopwatch
  Button 2 splits the time (freezes display)
  Button 3 resets the stopwatch to 0
    Only when stopped, no effect when counting
  Be precise (correct) with timing!
Submit this code to ReCodEx

## Slide 7: Stopwatch
Stopwatch states in more detail
  Button 2 works as lap time splitter
    Freezes display number, but the stopwatch goes on
    Only allowed when stopwatch is running
    Button 1 cannot stop the watch when time is lapped
  See the diagram below
stopped
running
B1
lapped
B3
B2
B2
B1

## Slide 8: Discussion