## Slide 1: NSWI170: Lab 06 Running Text Messages
Martin Kruliš

## Slide 2: Pointers, Arrays, and Strings
Pointers in C
  type *p = <pointer expression>
    nullptr – pointer to nowhere (special value)
    Taken as reference (address) of existing value (&)
    Computed from another pointer (pointer arithmetic)
    Memory allocation function/operator
      Use only static array allocation on Arduino (e.g., int a[4])
  int x = 42;
  int *p = &x;
  int y = *p + 54;
Creates space for 1 int and labels it x
Create pointer to int p (* declares pointer)
Reads value at p address and uses it in addition (* dereferences pointer)

## Slide 3: Pointers, Arrays, and Strings
Pointers in C
  Pointer arithmetic
  Pointers and Arrays
    Array ~ pointer at beginning
    int buf[42];
    buf[i] *(buf + i)
int
int
int
int
int
int
…
int *p
int *p2 = p+5
++p
Assuming the memory is already allocated!
(pointers do not allocate by themselves)
Combined memory allocation (42 ints in a block) and pointer creation (buf is int*)
Always use brackets [] when working with array, always use * when dereferencing pointer

## Slide 4: Pointers, Arrays, and Strings
Strings in C
  Array of chars, terminated by 0 (zero char)
  const char *str = "Arduino Uno";
  size_t some_function(const char *str) {
  size_t i = 0;
  while (str[i]) ++i;
  return i;
  }
A
r
d
u
i
n
o
U
n
o
\0
*str
What does this function do?
"\0" is added automatically

## Slide 5: Pointers, Arrays, and Strings
Pitfalls
  Uninitialized pointers
    int *p;
  Reaching beyond arrays
    int buf[5];
    int *p = buf + 5;
    *p = 42;
  Strings in fix-sized buffers (like char buf[32])
    Possible, but dangerous (must not overflow!!!)
    Do not forget to allocate space for trailing zero!
May hold random address – always initialize!
Huge mistake! Writing data right after buf array (where possibly some other variable is, but who knows?)

## Slide 6: Task
Create a running text message on LCD
  Download prepared starter pack and open it
  Message is sent over via serial link
    Use SerialInputHandler class
  Display multiplex works like in the last assignment
  Text scrolls (4 chars are visible at a time)
    Advance position every 300ms
    Loop the scrolling (once its gone, start over again)
  Use pointers in your code !!!
Final task In ReCodEx
H
i
p
p
o
i
s
g
r
e
a
t

## Slide 7: Discussion