## Slide 1: Practical Course in Computer Systems
Arduino, Arduino IDE, Funshield
Jakub Yaghob

## Slide 2: Arduino
Open-source HW and SW project
HW
  Arduino board – base board with sets of digital and analog pins
  Expansion board (shield) – connected by pins providing various functionality
SW
  Arduino IDE

## Slide 3: Arduino UNO
Entry level board
  CPU ATmega328P
  14 digital I/O pins
    Of which 6 can be used as PWM outputs
  6 analog inputs
  Clock speed 16 MHz
  FLASH memory 32 KB
  SRAM 2 KB
  EEPROM 1 KB
  USB
  DC power

## Slide 4: Arduino IDE
Sketch
  An application
Library
  Shared interface and implementation
Two important functions
  void setup() { }
    Called once at the start of a sketch
  void loop() { }
    Called repeatedly ~1000-times per sec

## Slide 5: How a sketch is executed
The sketch is compiled by a compiler in Arduino IDE for the target CPU
Resulting binary code is uploaded via USB/serial to an Arduino board and the board is reset
EEPROM on the board contains boot loader, which is executed after board reset
If there is some USB/serial payload after the reset, it is read by boot loader, stored to the FLASH memory on the board, and executed
If there is no payload, boot loader executes already stored sketch in the FLASH memory
Sketch .c
Binary code
Compile
USB/serial
FLASH
Bootloader
Write memory
Host
Arduino

## Slide 6: Funshield
Simple “interactive” shield
  3 buttons
  4 LEDs
  4-digit display
  1 buzzer – won’t be used, too noisy
  1 potentiometer – won’t be used, too small
  More info – follow the URL in the “Links” tab
Funshield library
  Download and unpack to your library folder

## Slide 7: Experiment – blink with LED
Initialize a LED
  pinMode(pin, OUTPUT/INPUT)
Blink with one chosen LED
  digitalWrite(pin, HIGH/LOW)
  delay(ms)
Blink without delay
  Use function unsigned long millis();
Blink with all LEDs
Display 4-bit binary number
  Increment continuously with some delay
Blink with all LEDs – snake
Bonus task: "antialiased" snake
  Last LED is dimming whilst the following one is lightening up
Notes: General comments:
Do not put all your code to one function. Use function decomposition.
Do not use switch command (or set of conditions) for a special code for one LED. Instead, use an array.
Beware of variable liveness! (local vs. global variables)
Use symbolic (named) constants. Do not use pin numbers directly.
The LED switches ON by writing LOW to the corresponding pin. And vice versa, the LED switches OFF by writing HIGH to the pin.
Specific comments for tasks:
You must initialize all LEDs, you will use in the task. Use pinMode system function.
Blink with one LED in a 1s period. [Write LOW to the selected pin using digitalWrite system function, stop the execution by using delay system function, then write HIGH to the selected pin, and use delay again.]
We do not want to use delay function, because it stops the execution of the loop. Instead, use system function millis for measuring time. [Remember initial time as a start time and set the initial state for the chosen LED. After a chosen time interval (always use test >=, not ==) change the state for the LED and remember the current time as a start time.]
The same task as task 3, but blink with all LEDs. Do not repeat your code, use array instead!
Display binary decomposition of the lowest 4 bits of a counter
Create "snake" pattern from all LEDs, i.e. blink LEDs sequentially. You may choose the pattern, i.e. either the snake is one-directional or it bounces forth and back.
Use handmade PWM (Pulse-Width Modulation), do not use built-in PWM, because it is not available for all LED pins.