## Slide 1: Practical Course in Computer Systems
Controlling LEDs with Buttons
Jakub Yaghob

## Slide 2: Bit Encoder
Revision
  pinMode(led1_pin, OUTPUT);
  digitalWrite(led1_pin, HIGH);
    HIGH ~ led is off, LOW ~ led is on
Task 1
  Write a function that takes integer and sets the LEDs according to its lowest 4 bits
    0 ~ led is off, 1 ~ led is on
    LSB on LED4, MSB on LED1
  Use the function to display some constants
    Just to verify it is working

## Slide 3: Continuous Counter
Task 2
  Create a counter that continuously increments its value (modulo 16)
    With reasonable interval, so it can be observed by humans
  Display the counter value using you function from Task 1

## Slide 4: Buttons
Setup
  pinMode(button1_pin, INPUT)
    Actually, this should be the default
Checking
  digitalRead(button1_pin)
    Inverse logic (false ~ button is pressed)
Task 3
  Counter should increment only when the button 1 is pressed

## Slide 5: Decrement
Task 4
  Make second button to work in a similar manner to the first one, only it will decrement the counter
  Note: How do you decrement in modulo arithmetic?
    x = (x + 15) % 16

## Slide 6: Counting Clicks
Task 5
  Change the behavior of the buttons
  Stop continuous increment/decrement
  The counter is incremented every time button 1 is pressed (or released, but not both)
  The counter is decremented every time button 2 is pressed

## Slide 7: Smart Buttons
Task 6
  Buttons will still increment/decrement the counter when pressed/released
  If the button is held for a while it starts to increment/decrement the counter continuously
Task 7
  Make the 3rd button behave like the first two, but it will add value 3 to the counter (modulo 16)

## Slide 8: Already Done?
Bonus tasks
  Remove the debouncing (20 ms)
  Make the third button switch between the three implemented strategies of updating the counter
  Allow the counter to grow from 0 to 256, the LEDs will alternate to show the lower 4 bits and higher 4 bits of the counter in an interval (if no button is pressed)