## Slide 1: Practical Course in Computer Systems
7-segment LED display – multiplex
Jakub Yaghob

## Slide 2: 4-digit number – naïve approach
Task 1
  Display all 4 digits simultaneously
  Do you observe any anomaly?
    If not, try to insert delay(2); to your loop function☻

## Slide 3: 4-digit number – correct version
Task 2
  Display only one digit in each loop
  Divide the interface for displaying a number
    void display_set_number(int num)
      Called once for a number, prepares display data
    void display_loop()
      Called in each loop iteration
    Shared state
      Object is an ideal encapsulation for this case, we won’t use it
  Don’t display leading zeroes
    12 is displayed as 12, not 0012

## Slide 4: Stopwatch – simple version
Task 3
  Stopwatch precision is 100 ms
  Always show at least 2 digits
    It starts on 0.0
  Use millis() function for correct timing
  B1 starts/stops stopwatch

## Slide 5: Stopwatch – reset
Task 4
  Like task 3
  Additionally, B3 resets stopwatch to 0.0
    Only if stopped

## Slide 6: Stopwatch – full version
Task 5
  Like task 4
  Additionally, B2 is a lap
    It freezes displayed number, but stopwatch counts on
    Only allowed when started
    B1 stop is only allowed when not lapped

## Slide 7: Stopwatch – state diagram
Stopped – stopwatch does not count, displays the last time
  Initially 0.0
  Can be reset by B3
Started – stopwatch counts, display current time
Lapped– stopwatch counts, the last time is displayed
stopped
started
B1
lapped
B3
B2
B2
B1