## Slide 1: Practical Course in Computer Systems
Use 7-segment LED display for text messages
Jakub Yaghob

## Slide 2: Pointers, Arrays, Strings
Pointers in C
  type *p = <pointer expression>
    nullptr
    Taken as reference to existing value (&)
    Computed from another pointer (pointer arithmetic)
    Memory allocation function/operator
      Not on Arduino
  int x = 42;
  int *p = &x;
  int y = *p + 54;

## Slide 3: Pointers, Arrays, Strings
Pointers in C
  Pointer arithmetic
  Pointers and arrays
    Array ~ pointer at beginning
    int buf[42]; buf[i] *(buf + i)
int
int
int
int
int
int
…
int *p
int *p2 = p+5
++p

## Slide 4: Pointers, Arrays, Strings
Strings in C
  Array of chars, terminated by 0
  const char *str = "Arduino Uno";
  size_t some_function(const char *str) {
  size_t i = 0;
  while (str[i]) ++i;
  return i;
  }
A
r
d
u
i
n
o
U
n
o
\0
*str
What does this function do?

## Slide 5: Today’s Task
Create a running text message on LCD
  Message is given as C-string
  Use displayChar() to display individual characters
    Multiplex
  Text scrolls (4 chars are visible at a time)
    Loop the scrolling (once its gone, start over again)
  Use pointers
H
i
p
p
o
i
s
g
r
e
a
t

## Slide 6: Extended Task
Use serial line to get the input
  Initialize serial line in setup
    Serial.begin(9600);
  Receive data from serial line
    serialEvent() or check Serial.available() periodically
    Serial.read() – get one char from the buffer
  Save received message to String and display it
  Devise a mechanism to clear the message (receive a new one)