## Slide 1
Chapter 3
Arithmetic for Computers
Original slides from:
https://www.slideshare.net/ececourse/chapter-3-3372943

## Slide 2: Arithmetic for Computers
Operations on integers


Addition and subtraction Multiplication and division Dealing with overflow

Floating-point real numbers
Representation and operations
§3.1 Introduction

## Slide 3: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction

Overflow if result out of range
Adding +ve and –ve operands, no overflow
Adding two +ve operands
  Overflow if result sign is 1
Adding two –ve operands
  Overflow if result sign is 0
Faster variant: book page 1197

## Slide 4: Integer Addition
§3.2 Addition and Subtraction
Faster variant: book page 1197
One-bit variant:

## Slide 5: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
+7:
–6:
+1:
0000 0000 … 0000 0111
1111 1111 … 1111 1010
0000 0000 … 0000 0001

Overflow if result out of range

Subtracting two +ve or two –ve operands, no overflow Subtracting +ve from –ve operand
Overflow if result sign is 0
Subtracting –ve from +ve operand
Overflow if result sign is 1


## Slide 6: Arithmetic for Multimedia
Graphics and media processing operates on vectors of 8-bit and 16-bit data
  Use 64-bit adder, with partitioned carry chain
    Operate on 8×8-bit, 4×16-bit, or 2×32-bit vectors
  SIMD (single-instruction, multiple-data)
Saturating operations
  On overflow, result is largest representable value
    c.f. 2s-complement modulo arithmetic
  E.g., clipping in audio, saturation in video

## Slide 7: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication

## Slide 8: Multiplication Hardware
Initially 0

## Slide 9: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff

Can be pipelined
Several multiplication performed in parallel

## Slide 10: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 11: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation


–2.34 × 1056
+0.002 × 10–4
+987.02 × 109

In binary
±1.xxxxxxx2 × 2yyyy

Types float and double in C
normalized
not normalized
§3.5 Floating Point

## Slide 12: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
Portability issues for scientific code Now almost universally adopted Two representations


Single precision (32-bit)
Double precision (64-bit)

## Slide 13: IEEE Floating-Point Format


S: sign bit (0  non-negative, 1  negative) Normalize significand: 1.0 ≤ |significand| < 2.0

Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
Significand is Fraction with the “1.” restored


Exponent: excess representation: actual exponent + Bias

Ensures exponent is unsigned
Single: Bias = 127; Double: Bias = 1203

S | Exponent | Fraction
single: 8 bits
double: 11 bits
single: 23 bits
double: 52 bits
x  (1)S (1Fraction) 2(ExponentBias)

## Slide 14: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value


Exponent: 00000001
 actual exponent = 1 – 127 = –126 (biased repr.)
Fraction: 000…00  significand = 1.0
±1.0 × 2–126 ≈ ±1.2 × 10–38

Largest value


exponent: 11111110
 actual exponent = 254 – 127 = +127
Fraction: 111…11  significand ≈ 2.0
±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 15: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value


Exponent: 00000000001
 actual exponent = 1 – 1023 = –1022
Fraction: 000…00  significand = 1.0
±1.0 × 2–1022 ≈ ±2.2 × 10–308

Largest value


Exponent: 11111111110
 actual exponent = 2046 – 1023 = +1023
Fraction: 111…11  significand ≈ 2.0
±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 16: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23

Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
Double: approx 2–52

Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 17: Floating-Point Example
Represent –0.75



–0.75 = (–1)1 × 1.12 × 2–1
S = 1
Fraction = 1000…002
Exponent = –1 + Bias

Single: –1 + 127 = 126 = 011111102
Double: –1 + 1023 = 1022 = 011111111102

Single: 1011111101000…00 Double: 1011111111101000…00


## Slide 18: Floating-Point Example
What number is represented by the single- precision float
11000000101000…00


S = 1
Fraction = 01000…002
Exponent = 100000012 = 129

x = (–1)1 × (1 + .012) × 2(129 – 127)
= (–1) × 1.25 × 22
= –5.0

## Slide 19: Denormal Numbers
Exponent = 000...0  hidden bit is 0
x  (1)S (0 Fraction) 2Bias
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
x  (1)S (0  0) 2Bias  0.0
Two representations of 0.0!

## Slide 20: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check

Exponent = 111...1, Fraction ≠ 000...0
Not-a-Number (NaN)
Indicates illegal or undefined result
  e.g., 0.0 / 0.0
Can be used in subsequent calculations

## Slide 21: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101

Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
Normalize result & check for over/underflow
  1.0015 × 102
Round and renormalize if necessary
  1.002 × 102



## Slide 22: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1

Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625



## Slide 23: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions

FP adder usually takes several cycles
Can be pipelined

## Slide 24: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 25: Floating-Point Multiplication
Consider a 4-digit decimal example

1.110 × 1010 × 9.200 × 10–5

1. Add exponents

For biased exponents, subtract bias from sum New exponent = 10 + –5 = 5


2. Multiply significands

1.110 × 9.200 = 10.212  10.212 × 105

3. Normalize result & check for over/underflow

1.0212 × 106

4. Round and renormalize if necessary

1.021 × 106

5. Determine sign of result from signs of operands

+1.021 × 106

## Slide 26: Floating-Point Multiplication
Now consider a 4-digit binary example

1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)

1. Add exponents

Unbiased: –1 + –2 = –3
Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127


2. Multiply significands

1.0002 × 1.1102 = 1.1102  1.1102 × 2–3

3. Normalize result & check for over/underflow

1.1102 × 2–3 (no change) with no over/underflow

4. Round and renormalize if necessary

1.1102 × 2–3 (no change)

5. Determine sign: +ve × –ve  –ve

–1.1102 × 2–3 = –0.21875

## Slide 27: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder

But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does


Addition, subtraction, multiplication, division, reciprocal, square-root
FP  integer conversion

Operations usually takes several cycles
Can be pipelined

## Slide 28: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA

Separate FP registers

32 single-precision: $f0, $f1, … $f31
Paired for double-precision: $f0/$f1, $f2/$f3, …
Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s

FP instructions operate only on FP registers

Programs generally don’t do integer ops on FP data, or vice versa
More registers with minimal code-size impact

FP load and store instructions
lwc1, ldc1, swc1, sdc1
  e.g., ldc1 $f8, 32($sp)

## Slide 29: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6

Double-precision arithmetic
add.d, sub.d, mul.d, div.d
  e.g., mul.d $f4, $f4, $f6

Single- and double-precision comparison

c.xx.s, c.xx.d (xx is eq, lt, le, …) Sets or clears FP condition-code bit
e.g. c.lt.s $f3, $f4

Branch on FP condition code true or false
bc1t, bc1f
  e.g., bc1t TargetLabel

## Slide 30: Interpretation of Data
Bits have no inherent meaning

Interpretation depends on the instructions applied
Computer representations of numbers

Finite range and precision
Need to account for this in programs
The BIG Picture

## Slide 31: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
§3.6 Parallelism and Computer Arithmetic: Associativity
 |  | (x+y)+z | x+(y+z)
x | -1.50E+38 | 0.00E+00 | -1.50E+38
y | 1.50E+38 |  | 1.50E+38
z | 1.0 | 1.0 | 
 |  | 1.00E+00 | 0.00E+00

Need to validate parallel programs under varying degrees of parallelism

## Slide 32: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands


2 × 64-bit double precision 4 × 32-bit double precision
Instructions operate on them simultaneously
Single-Instruction Multiple-Data

## Slide 33: Right Shift and Division

Left shift by i places multiplies an integer by 2i
Right shift divides by 2i?
Only for unsigned integers
For signed integers


Arithmetic right shift: replicate the sign bit e.g., –5 / 4

111110112 >> 2 = 111111102 = –2
Rounds toward –∞

c.f. 111110112 >>> 2 = 001111102 = +62
§3.8 Fallacies and Pitfalls